## Slide 1: Mobile Communications Chapter 3: Medium Access
Motivation
SDMA, FDMA, TDMA, CDMA
Aloha, reservation schemes
Collision avoidance, MACA
Polling
Comparison

## Slide 2: Motivation
Can we apply media access methods from fixed networks?
Example CSMA/CD
  Carrier Sense Multiple Access with Collision Detection
  send as soon as the medium is free, listen into the medium if a collision occurs (legacy method in IEEE 802.3)
Problems in wireless networks
  signal strength decreases proportional to (at least) the square of the distance
  the sender would apply CS and CD, but the collisions happen at the receiver
  it might be the case that a sender cannot “hear” the collision, i.e., CD does not work
  furthermore, CS might not work if, e.g., a terminal is “hidden”

## Slide 3: Problem of CSMA/CD in wireless communication
noise
sender C
receiver B
sender A
signal strength
threshold
signal ok
signal ok
collision

## Slide 4: Motivation - hidden and exposed terminals
Hidden terminals
  A sends to B, C cannot receive A
  C wants to send to B, C senses a “free” medium (CS fails)
  collision at B, A cannot receive the collision (CD fails)
  A is “hidden” for C
Exposed terminals
  B sends to A, C wants to send to another terminal (not A or B)
  C has to wait, CS signals a medium in use
  but A is outside the radio range of C, therefore waiting is not necessary
  C is “exposed” to B
B
A
C

## Slide 5: Motivation - near and far terminals
Terminals A and B send, C receives
  signal strength decreases proportional to the square of the distance
  the signal of terminal B therefore drowns out A’s signal
  C cannot receive A
If C for example was an arbiter for sending rights, terminal B would drown out terminal A already on the physical layer
Also severe problem for CDMA-networks - precise power control needed!
A
B
C

## Slide 6: Access methods SDMA/FDMA/TDMA
SDMA (Space Division Multiple Access)
  segment space into sectors, use directed antennas
  cell structure
FDMA (Frequency Division Multiple Access)
  assign a certain frequency to a transmission channel between a sender and a receiver
  permanent (e.g., radio broadcast), slow hopping (e.g., GSM), fast hopping (FHSS, Frequency Hopping Spread Spectrum)
TDMA (Time Division Multiple Access)
  assign the fixed sending frequency to a transmission channel between a sender and a receiver for a certain amount of time
PDMA (Polarization Division Multiple Access)
  assign a certain polarization to a transmission channel using, e.g. specialized antennas
The multiplexing schemes presented in chapter 2 are now used to control medium access!
  multiplexing scheme plus algorithm  Multiple Access method
Notes: 15

## Slide 7: FDD/FDMA - general scheme, example GSM
FDM used twice
  FDD (Frequency Division Duplex)
    separation of the direction (uplink/downlink) using different frequencies
  FDMA
    separation of different channels using different frequencies
f
t
124
1
124
1
20 MHz
200 kHz
890.2 MHz
935.2 MHz
915 MHz
960 MHz

## Slide 8: OFDMA – Orthogonal frequency-division multiple access
Use OFDM for multiple access, i.e. assign sub-carriers to individual users for a certain time
  can be seen as combination of FDM and TDM
  OFDM uses FDM with “orthogonal” carriers, i.e. multiple closely spaced subcarrier signals with overlapping spectra are transmitted to carry data in parallel (See e.g. DVB, DAB+, DSL, IEEE 802.11a, …)
  used in e.g. IEEE 802.11ax, LTE, 5G New Radio
Advantages
  high flexibility (data rates, frequencies, QoS)
  can fill white spaces (see CR)
  good robustness wrt. fading and interference
  shorter/constant delay
Disadvantages
  more complex electronics with FFT, FEC
  frequency-selective fading if few subcarriers used
  co-channel interference from neighboring cells
subcarrier
number
1
7
21
26
-26
-21
-7
-1
channel center frequency
subcarrier spacing
pilot

## Slide 9: TDD/TDMA - general scheme, example DECT
TDM used twice
  TDD (Frequency Division Duplex)
    separation of the direction (uplink/downlink) using different time periods
  TDMA
    separation of different channels using different time-slots
  Please note!
  other combinations can also make sense
  TDD, TDMA, FDM: WLANs following 802.11 offering several channels, up- and downlink on same channel, users separated in time
  FDD, TDMA: GSM when looking at users on a certain channel, up- and downlink separated in frequency, users separated in time
  …
1
2
3
11
12
1
2
3
11
12
t
downlink
uplink
417 µs

## Slide 10: Questions & Tasks
  What is the main physical reason for the failure of many MAC schemes known from wired networks? What is done in wired networks to avoid this effect?
  What is the basic prerequisite for applying FDMA? How does this factor increase complexity compared to TDMA systems?
  Who is responsible for MAC if we consider the whole frequency spectrum as presented in chapter 1?
  Considering duplex channels, what are alternatives for implementation in wireless networks? What about typical wired networks?
  Assume all stations can hear all other stations. One station wants to transmit and senses the carrier idle. Why can a collision still occur after the start of transmission?

## Slide 11: Aloha/slotted aloha
Mechanism
  random, distributed (no central arbiter), time-multiplex
  Slotted Aloha additionally uses time-slots, sending must always start at slot boundaries
Aloha
Slotted Aloha
sender A
sender B
sender C
collision
sender A
sender B
sender C
collision
t
t

## Slide 12: DAMA - Demand Assigned Multiple Access
Channel efficiency only 18% for Aloha, 36% for Slotted Aloha
  assuming Poisson distribution for packet arrival and packet length
Reservation can increase efficiency to 80%
  a sender reserves a future time-slot
  sending within this reserved time-slot is possible without collision
  reservation also causes higher delays
  typical scheme for satellite links
Examples for reservation algorithms:
  Explicit Reservation according to Roberts (Reservation-ALOHA)
  Implicit Reservation (PRMA)
  Reservation-TDMA

## Slide 13: Access method DAMA: Explicit Reservation
Explicit Reservation (Reservation Aloha):
  two modes:
    ALOHA mode for reservation: competition for small reservation slots, collisions possible
    reserved mode for data transmission within successful reserved slots (no collisions possible)
  it is important for all stations to keep the reservation list consistent at any point in time and, therefore, all stations have to synchronize from time to time
Aloha
reserved
Aloha
reserved
Aloha
reserved
Aloha
collision
t
Notes: 24

## Slide 14: Access method DAMA: PRMA
Implicit reservation (PRMA - Packet Reservation MA):
  a certain number of slots form a frame, frames are repeated
  stations compete for empty slots according to the slotted aloha principle
  once a station reserves a slot successfully, this slot is automatically assigned to this station in all following frames as long as the station has data to send
  competition for this slots starts again as soon as the slot was empty in the last frame
frame1
frame2
frame3
frame4
frame5
1
2
3
4
5
6
7
8
time-slot
collision at reservation attempts
A
C
D
A
B
A
F
A
C
A
B
A
A
B
A
F
A
B
A
F
D
A
C
E
E
B
A
F
D
t
ACDABA-F
ACDABA-F
AC-ABAF-
A---BAFD
ACEEBAFD
reservation
Notes: 25

## Slide 15: Access method DAMA: Reservation-TDMA
Reservation Time Division Multiple Access
  every frame consists of N mini-slots and x data-slots
  every station has its own mini-slot and can reserve up to k data-slots using this mini-slot (i.e. x = N * k).
  other stations can send data in unused data-slots according to a round-robin sending scheme (best-effort traffic)
N mini-slots
N * k data-slots
reservations for data-slots
other stations can use free data-slots
based on a round-robin scheme
e.g. N=6, k=2
Notes: 26

## Slide 16: MACA - collision avoidance
MACA (Multiple Access with Collision Avoidance) uses short signaling packets for collision avoidance
  RTS (request to send): a sender request the right to send from a receiver with a short RTS packet before it sends a data packet
  CTS (clear to send): the receiver grants the right to send as soon as it is ready to receive
Signaling packets contain
  sender address
  receiver address
  packet size
Variants of this method can be found in IEEE802.11 as DFWMAC (Distributed Foundation Wireless MAC)

## Slide 17: MACA examples
MACA avoids the problem of hidden terminals
  A and C want to send to B
  A sends RTS first
  C waits after receiving CTS from B
MACA avoids the problem of exposed terminals
  B wants to send to A, C to another terminal
  now C does not have to wait for it, cannot receive CTS from A
A
B
C
RTS
CTS
CTS
A
B
C
RTS
CTS
RTS

## Slide 18: Polling mechanisms
If one terminal can be heard by all others, this “central” terminal (a.k.a. base station) can poll all other terminals according to a certain scheme
  now all schemes known from fixed networks can be used (typical mainframe - terminal scenario)
Example: Randomly Addressed Polling
  base station signals readiness to all mobile terminals
  terminals ready to send can now transmit a random number without collision with the help of CDMA or FDMA (the random number can be seen as dynamic address)
  the base station now chooses one address for polling from the list of all random numbers (collision if two terminals choose the same address)
  the base station acknowledges correct packets and continues polling the next terminal
  this cycle starts again after polling all terminals of the list

## Slide 19: ISMA (Inhibit Sense Multiple Access)
Current state of the medium is signaled via a “busy tone”
  the base station signals on the downlink (base station to terminals) if the medium is free or not
  terminals must not send if the medium is busy
  terminals can access the medium as soon as the busy tone stops
  the base station signals collisions and successful transmissions via the busy tone and acknowledgements, respectively (media access is not coordinated within this approach)
  classical mechanism used, e.g., for CDPD (USA, integrated into AMPS)

## Slide 20: Questions & Tasks
  Recall the problem of hidden and exposed terminals. What happens in the case of such terminals if Aloha, slotted Aloha, reservation Aloha, or MACA is used?
  What are the advantages of a fixed TDM pattern compared to random, demand driven TDM? Compare the efficiency in the case of several connections with fixed data rates or in the case of varying data rates. Now explain why traditional mobile phone systems use fixed patterns, while computer networks generally use random patterns. The major part of data being transmitted is computer-generated data. How has this fact changed mobile phone systems?
  What are benefits of reservation schemes? How are collisions avoided during data transmission, why is the probability of collisions lower compared to classical Aloha? What are disadvantages of reservation schemes?
  How can MACA still fail in case of hidden/exposed terminals? Think of mobile stations and changing transmission characteristics.

## Slide 21: Access method CDMA
CDMA (Code Division Multiple Access)
  all terminals send on the same frequency probably at the same time and can use the whole bandwidth of the transmission channel
  each sender has a unique random number, the sender XORs the signal with this random number
  the receiver can “tune” into this signal if it knows the pseudo random number, tuning is done via a correlation function
Disadvantages:
  higher complexity of a receiver (receiver cannot just listen into the medium and start receiving if there is a signal)
  all signals should have the same strength at a receiver
Advantages:
  all terminals can use the same frequency, no planning needed
  huge code space (e.g. 232) compared to frequency space
  interferences (e.g. white noise) is not coded
  forward error correction and encryption can be easily integrated
Notes: 28

## Slide 22: CDMA in theory (very simplified)
Sender A
  sends Ad = 1, key Ak = 010011 (assign: “0”= -1, “1”= +1)
  sending signal As = Ad * Ak = (-1, +1, -1, -1, +1, +1)
Sender B
  sends Bd = 0, key Bk = 110101 (assign: “0”= -1, “1”= +1)
  sending signal Bs = Bd * Bk = (-1, -1, +1, -1, +1, -1)
Both signals superimpose in space
  interference neglected (noise etc.)
  As + Bs = (-2, 0, 0, -2, +2, 0)
Receiver wants to receive signal from sender A
  apply key Ak bitwise (inner product)
    Ae = (-2, 0, 0, -2, +2, 0)  Ak = 2 + 0 + 0 + 2 + 2 + 0 = 6
    result greater than 0, therefore, original bit was “1”
  receiving B
    Be = (-2, 0, 0, -2, +2, 0)  Bk = -2 + 0 + 0 - 2 - 2 + 0 = -6, i.e. “0”

## Slide 23: CDMA on signal level I (still pretty simplified)
data A
key A
signal A
data  key
key
sequence A
Real systems use much longer keys resulting in a larger distance
between single code words in code space.
1
0
1
1
0
0
1
0
0
1
0
0
0
1
0
1
1
0
0
1
1
0
1
1
0
1
1
1
0
0
0
1
0
0
0
1
1
0
0
Ad
Ak
As

## Slide 24: CDMA on signal level II
signal A
data B
key B
key
sequence B
signal B
As + Bs
data  key
1
0
0
0
0
0
1
1
0
1
0
1
0
0
0
0
1
0
1
1
1
1
1
1
0
0
1
1
0
1
0
0
0
0
1
0
1
1
1
Bd
Bk
Bs
As

## Slide 25: CDMA on signal level III
Ak
(As + Bs) * Ak
integrator
output
comparator
output
As + Bs
data A
1
0
1
1
0
1
Ad

## Slide 26: CDMA on signal level IV
integrator
output
comparator
output
Bk
(As + Bs) * Bk
As + Bs
data B
1
0
0
1
0
0
Bd

## Slide 27: CDMA on signal level V
comparator
output
wrong
key K
integrator
output
(As + Bs) * K
As + Bs
(0)
(0)
?

## Slide 28: SAMA - Spread Aloha Multiple Access
Aloha has only a very low efficiency, CDMA needs complex receivers to be able to receive different senders with individual codes at the same time
Idea: use spread spectrum with only one single code (chipping sequence) for spreading for all senders accessing according to aloha
1
sender A
0
sender B
0
1
t
narrow band
send for a
shorter period
with higher power
spread the signal e.g. using the chipping sequence 110101 („CDMA without CD“)
Problem: find a chipping sequence with good characteristics
1
1
collision

## Slide 29: Comparison SDMA/TDMA/FDMA/CDMA

## Slide 30: Questions & Tasks
  How does the near/far effect influence TDMA systems? What happens in CDMA systems? What are countermeasures in TDMA systems, what about CDMA systems?
  Who performs the MAC algorithm for SDMA? What could be possible roles of mobile stations, base stations, and planning from the network provider?
  Explain the term interference in the space, time, frequency, and code domain. What are countermeasures in SDMA, TDMA, FDMA, and CDMA systems?
  Which of the MAC schemes can give hard guarantees related to bandwidth and access delay?
  How are guard spaces realised between users in CDMA?
  Redo the simple CDMA example, but now add random ‘noise’ to the transmitted signal (–2,0,0,–2,+2,0). Add, for example, (1,–1,0,1,0,–1). In this case, what can the receiver detect for sender A and B respectively? Now include the near/far problem. How does this complicate the situation? What would be possible countermeasures?